Finding innovations from the time series in MA(1) model
Baruch Youssin
January 4, 2022
# Moving average model
The moving average model of order 1, MA(1), is specified by the following formula:
(1) X_{t}=c+%varepsilon _{t}+%theta _{1}%varepsilon _{t-1}
where %varepsilon _{t} , t = …, -1, 0, 1, … are innovations (white noise), c and %theta _{1} (where abs%theta _{1}<1 ) are parameters of the model, and X_{t} is the time series generated by the model; see Wikipedia.
To specify the model, we also need to specify the parameters of the innovations %varepsilon _{t} . Usually they are taken to be independently normally distributed with zero mean, and their standard deviation %sigma is another parameter of the model.
# Does a given time series fit the model?
Given a finite time series, we can ask, whether it is generated by such model with the specified values of the parameters.
While the given series is finite, we are interested, whether it is a part of an infinite series generated by this model.
In fact, this is always possible, and in many possible ways, as the linear system (1) is indeterminate; the correct question is whether such sequence is likely to be generated by this model.
It is likely if the innovation values are not too large in comparison with the standard deviation %sigma ; this is quantified by the likelihood which is equal to the probability density of the joint probability distribution of all %varepsilon _{t} at the innovation values we have found.
The log likelihood is given (up to an additive constant) by - {{1} over {2 %sigma ^2}} (sum %varepsilon^2_{t}) . It follows that maximizing the log likelihood amounts to the least square principle for the innovation values.
### A note on the usage of maximal likelihood principle
Note that we already use the maximal likelihood principle at this point. In case of Bayesian approach, we probably need to integrate the likelihood over all possible innovations that generate our series. The result appears to be related to the maximal likelihood by a multiplicative constant.
# The matrix equation on the innovation values
Suppose we are given a time series X_0,X_1,...,X_n . It is defined by the innovation values %varepsilon_{-1},%varepsilon_0,%varepsilon_1,...,%varepsilon_n by the equation
(2) A %varepsilon = widehat {X}
where
%varepsilon =left( { stack{%varepsilon_{-1} # %varepsilon_0 # %varepsilon_1 #.#.#%varepsilon_n} } right) , widehat {X} =left( { stack{X_0 -c# X_1 -c#.#.#X_n -c} } right) , A=left( { matrix{%theta _1 # 1 # 0 # ... # ... ## 0 # %theta _1 # 1 # 0 # ... ## 0 # 0 # %theta _1 # 1 # ... ## ... # ... # ... # ... # ...} } right)
and the size of A is (n + 1) x (n + 2) (n + 1 rows and n + 2 columns).
Clearly, the rank of A is n + 1 and the solution always exists.
# Summary
Thus, to find the innovation values, we need to find the least-square solution of the linear system (2).
# Multiple pieces of a time series
Suppose we are given a few contiguous time blocks of a time series, say, X_0,X_1,...,X_{n_1},X_{n_2},...,X_{n_3},X_{n_4},...,X_{n_m}
As in case of one time block, we want to know how likely it is that these blocks belong to a time series generated by a MA(1) model with specified parameters.
To this end, we need to find the innovation values that generate these time blocks.
# Naive approach
Each block X_{n_k},...,X_{n_{k+1}} is generated by %varepsilon _{n_k-1}, %varepsilon _{n_k},...,%varepsilon _{n_{k+1}} .
We assume that the blocks are separated one from the other by at least one element; it follows that the blocks of innovations %varepsilon _{n_k-1}, %varepsilon _{n_k},...,%varepsilon _{n_{k+1}} do not overlap.
We can find each of these blocks %varepsilon _{n_k-1}, %varepsilon _{n_k},...,%varepsilon _{n_{k+1}} from its respective block X_{n_k},...,X_{n_{k+1}} as explained above, and this yields all the innovation values that we need.
The problem with this approach appears in the following case:
The blocks are not far one from another ( n_{ k+2 } is not far from n_{ k+1 } ) while X_{n_{k+2}}-X_{n_{k+1}} is not small in comparison with %sigma SQRT{n_{ k+2 } - n_{ k+1 }} .
In such case the values of %varepsilon _{n_{k+1}+1}, ...,%varepsilon _{n_{k+2}-2} may have to be large to generate the entire sequence that includes these blocks.
Thus, even if the innovation values that generate each block, may be likely, the innovation values that are needed to get from one block to another, may turn out to be unlikely.
# A better approach
Try to find all the values of innovations %varepsilon_{-1},%varepsilon_0,%varepsilon_1,...,%varepsilon_{n_m} that are needed to generate the time series X_0,X_1,...,X_{n_m} that includes that gaps between the blocks.
To this end, we need to solve the system (2) in which we do not know the values of some of the coordinates of the vector widehat {X} in its right-hand side.
The equations in this system whose right-hand sides we do not know, need to be removed (they correspond to the gaps between the blocks).
With this removal, the system becomes even more indeterminate than before; it still has multiple solutions.
The least square solution can still be found.
For the measure of likelihood of this solution, we should take sum from{i=-1} to{n_m} {%varepsilon _i^2} including the innovations between the blocks, as they are necessary to get from one block to the other.