Maximal likelihood parameters for ARIMA(0,1,1) model
Baruch Youssin
January 6, 2022
# ARIMA(0,1,1) model
This model for a time series Y _{t} , t = …, -1, 0, 1, …, is characterized by the requirement that the first differences of the time series are generated by the Moving Average model of order 1, MA(1).
The parameters of ARIMA(0,1,1) model are the initial value of the series (or any other element of the series, chosen in advance) and the parameters of MA(1).
As the initial value is known, it remains to estimate the parameters of MA(1) from the first differences of the original time series.
We denote these first differences by X _{t} = Y _{t+1} - Y _{t} , t = …, -1, 0, 1, …
At this point we can forget our original time series Y _{t} and concentrate on its first differences X _{t} .
The MA(1) model is described by the following formula:
(1) X_{t}=c+%varepsilon _{t}+%theta _{1}%varepsilon _{t-1}
where %varepsilon _{t} , t = …, -1, 0, 1, …, are innovations (white noise), c and %theta _{1} (where abs%theta _{1}<1 ) are parameters of the model, and X_{t} is the time series generated by the model; see Wikipedia.
To specify the model, we also need to specify the parameters of the innovations %varepsilon _{t} . Usually they are taken to be independently normally distributed with zero mean, and their standard deviation %sigma is another parameter of the model.
Thus, the parameters of the model are c, %theta _{1} (satisfying abs%theta _{1}<1 ) and %sigma .
# Maximal likelihood estimation of the parameters
Given a finite time series X _{t} , we can ask, what are the values of the parameters c, %theta _{1} and %sigma that generate such series with the maximal likelihood; the likelihood is defined as the probability density of generating X _{t} with the specified values of the parameters.
While the given series is finite, we are considering the probability density of it being generated as a part of an infinite series generated by this model.
# The innovation values are not unique
Suppose we are given a time series Y_0,Y_1,...,Y_{ n+1 } with the differences X_0,X_1,...,X_n . It is defined by the innovation values %varepsilon_{-1},%varepsilon_0,%varepsilon_1,...,%varepsilon_n which are not unique.
Thus, while the model is described by the distribution of the innovations %varepsilon_{-1},%varepsilon_0,%varepsilon_1,...,%varepsilon_n , we cannot determine the (joint) probability density X_0,X_1,...,X_n as the probability density of any innovation values.
# The covariance matrix
The model MA(1) implies that the vector (X_0,X_1,...,X_n) is normally distributed with the center c,c,...,c and the following covariance matrix:
E( (X_t-c)^{2} ) = E( (%varepsilon _{t}+%theta _{1}%varepsilon _{t-1})^{2} )=( %theta _{1}+1 )%sigma ,
 E( (X_t-c) (X_{t-1}-c)) = E( (X_{t-1}-c) (X_t-c) ) = E( (%varepsilon _{t}+%theta _{1}%varepsilon _{t-1}) (%varepsilon _{t-1}+%theta _{1}%varepsilon _{t-2}) )= %theta _{1} %sigma ,
 E( (X_{t_1}-c) (X_{t_2}-c)) = 0 in all other cases,
Cov= %sigma left( { matrix{ %theta _1 + 1 # %theta _1 # 0 # ... ## %theta _1 # %theta _1 + 1 # %theta _1 # ... ## 0 # %theta _1 # %theta _1 + 1 # ... ## ... # ... # ... # ...} } right) .
# The likelihood
The probability density of X=(X_0,X_1,...,X_n) is given by
{exp left(- {1 over 2}left(X-c widehat {1} right) Cov^{-1} left(X-c widehat {1} right)^{T} right)} over {SQRT {(2 %pi )^{n+1} det (Cov)}}
where widehat {1} =(1,1,...,1) and the superscript T indicates matrix transpose.
It follows that maximal likelihood is equivalent to minimization of the loss which is the log-likelihood multiplied by (-2), up to an additive constant:
loss = left(X-c widehat {1} right) Cov^{-1} left(X-c widehat {1} right)^{T} + log det (Cov) .
This loss is minimized with respect to the parameters c, %theta _{1} (satisfying abs%theta _{1}<1 ) and %sigma .
# On estimating the constant c
A recent reference Umberto Triacca suggests estimating c as the expectation of X: {1} over {n+1} sum from{t=0} to{n} X_t = {X . {widehat {1}}^{T} } over {n+1} where X . {widehat {1}}^{T} is the (dot) product of X with the vector widehat {1} .
The logic behind this suggestion is clear: c is the expectation of the process that yields X, and we can estimate it in this way.
However, this estimation may be different from the estimation by the maximal likelihood principle (by minimizing the loss as above), as follows.
Minimizing the above loss with respect to only c yields the equation
-widehat {1} Cov^{-1} left(X-c widehat {1} right)^{T}- left(X-c widehat {1} right) Cov^{-1} {widehat {1}}^{T} = 0 ,
c= {X Cov^{-1} {widehat {1}}^{T}} over { widehat {1} Cov^{-1} {widehat {1}}^{T}}
One can see that for large n (large in comparison with {%theta _1 + 1} over {%theta _1 } ) this value of c is close to {X . {widehat {1}}^{T} } over {n+1} .
Indeed, the matrix Cov is Toeplitz; it is the matrix of a discrete convolution with a kernel of size 3. Hence, its inverse is also Toeplitz, the matrix of a discrete convolution with a kernel K of large size whose elements decrease away from its center. The denominator { widehat {1} Cov^{-1} {widehat {1}}^{T}} is approximately (n + 1) times the sum of the elements of this kernel while the numerator {X Cov^{-1} {widehat {1}}^{T}} is obtained by first applying the convolution with K to X – replacing each X_t with a linear combination of nearby elements – and then taking the sum of all elements of the result. If n is much larger than the size of the essential support of K (of the region where the elements of K are not negligible) then {X Cov^{-1} {widehat {1}}^{T}} is approximately the product of the sum of the elements of X (this is X . {widehat {1}}^{T} ) and the sum of the elements of the kernel, and the ratio c= {X Cov^{-1} {widehat {1}}^{T}} over { widehat {1} Cov^{-1} {widehat {1}}^{T}} is close to {X . {widehat {1}}^{T} } over {n+1} .
However, when n is not so large, there could be a difference.
# Multiple pieces of a time series
Suppose we are given a few contiguous time blocks of a time series, say, Y_0,Y_1,...,Y_{n_1+1},Y_{n_2},...,Y_{n_3+1},Y_{n_4},...,Y_{n_m+1} .
As in case of one time block, we want to estimate the parameters of an ARIMA(0,1,1) model that generates the series containing these blocks.
These parameters consist of the parameters of the MA(1) model, c, %theta _{1} (satisfying abs%theta _{1}<1 ) and %sigma , and any one element Y_t of the time series, chosen in advance.
When we take the differences of this series, we need to take the differences within the blocks and the differences between the blocks:
X_0 = Y_1 - Y_0 , X_1 = Y_2 - Y_1 , …, X_{n_1} = Y_{n_1+1} - Y_{n_1} , X_{n_1+1 %tendto n_2-1} = Y_{n_2} - Y_{n_1+1} , X_{n_2}=Y_{n_2+1} - Y_{n_2} , …, X_{n_m} = Y_{n_m+1} - Y_{n_m}
We have
X_{n_1+1 %tendto n_2-1} = X_{n_1+1 } + X_{n_1+2} +...+X_{n_2-1} .
It follows that the vector (X_0,X_1,...,X_{n_1},X_{n_1+1 %tendto n_2-1},X_{n_2},...,X_{n_m}) is normally distributed.
Its center is determined by the expectations
E(X_t)=c for all t, and
E(X_{n_1+1 %tendto n_2-1})=( n_2-n_1-1 )c (similarly for the other gaps),
Its covariance matrix can be found from the following equalities:

E( (X_t-c)^{2} ) = ( %theta _{1}+1 )%sigma and E( (X_t-c) (X_{t-1}-c)) = %theta _{1} %sigma as before,

E( (X_{n_1+1 %tendto n_2-1}-E(X_{n_1+1 %tendto n_2-1}))^{2} ) = ( n_2-n_1-1 )( %theta _{1}+1 )%sigma + 2( n_2-n_1-2 ) %theta _{1} %sigma left none right none = left( ( 3n_2-3n_1-5 ) %theta _{1} + n_2-n_1-1 right) %sigma and similarly for the other gaps,
 E( (X_{n_1+1 %tendto n_2-1}-E(X_{n_1+1 %tendto n_2-1})) (X_{n_1}-c)) = %theta _{1} %sigma and similarly for the other gaps,
E( (X_{n_2}-c) (X_{n_1+1 %tendto n_2-1}-E(X_{n_1+1 %tendto n_2-1}))) = %theta _{1} %sigma and similarly for the other gaps.
If we denote this covariance matrix by Cov, the above formulas for the probability density and for the loss remain valid.